## Slide 1: Estructura de Datos y Algoritmos
ITBA 2025-Q1

## Slide 2: Colisiones
Existen 2 formas de resolver las colisiones:
Open Addressing or Closed Hashing: dentro de la misma tabla de hashing se guardan los elementos que colisionaron
Open Hashing or Closed Addressing or Chaining => fuera del hashing se almacenan los elementos que colisionaron.

## Slide 3: Open Addressing or Closed Hashing
Cada ranura puede tener null (está vacío o baja física). Aunque la ranura no esté vacía puede ser que el elemento no esté, ya que hay que manejar el concepto de bajas lógicas (además de las físicas). Es decir, una ranura representa 3 estados: tiene un elemento o no tiene un elemento (dado por baja lógica o bien por baja física).
Típica formas de resolver esa colisión:
  Rehasheo Lineal (linear probing). Si hay colisión en la ranura i, entonces intentar con la ranura i+1, y así siguiendo hasta encontrar que el elemento (se hace update) o encontrar un lugar vacío (baja física) y se inserta allí. Con esta técnica si hay lugar lo encuentra seguro.
  Ej: si cae en ranura 4 y está ocupado va a intentar ranura 4+1, luego ranura 4+1+1, luego ranura 4+1+1+1, etc. Se suele tratar al arreglo como una lista circular.
  Resaheo Cuadrático (quadratic probing). El intervalo entre ranuras a usar, si hubiera colisión, será cuadrática. Ej: si le toca la ranura 4 y está ocupado, va intentar la ranura 4+1*1, luego 4+2*2, luego 4+3*3, etc. Problema: podría haber lugar y no lo encuentra.
  Otra combinación predeterminada (determinística) de fn: siempre conviene que la última sea rehasheo lineal.

## Slide 4
Supongamos que quiero rehasheo lineal

## Slide 5: Open Addressing or Closed Hashing
Borrado: No se puede reemplazar al lugar borrado por una ranura vacía porque la búsqueda de alguna clave puede necesitar "pasar sobre ella" si hubo colisión. Se debe manejar dos tipos de borrado: físico ( realmente se elimina el elemento ) y lógico ( se lo marca como que no está, y si más tarde hay que insertar en esa ranura se la puede aprovechar).
  El borrado físico se lo usa cuando la ranura que le sigue está también borrado físicamente
  El borrado lógico se lo usa en caso contrario, o sea cuando la ranura que le sigue está ocupada o bien borrada lógicamente

## Slide 6: Open Addressing or Closed Hashing
Búsqueda: Por lo dicho en el punto anterior se comienza buscando la clave en la ranura calculada. Si el lugar está con baja física seguro que no está en otro lado. Caso contrario si está marcado como ocupado y coincide con el valor esperado, se ha encontrado!!!. Pero si el lugar está ocupado y no es el elemento buscado o bien está como baja lógica, no se sabe si va aparecer más adelante (en la aplicación de las sucesivas funciones de hashing). O sea que en ese caso hay que seguir buscando hasta encontrarlo (hallar una ranura ocupada que coincida con el elemento) o bien hallar una baja física.

## Slide 7: Open Addressing or Closed Hashing
Inserción: Si la ranura calculada está marcada como baja física, el elemento se inserta allí. Caso contrario (está ocupado y no es el elemento a insertar, o bien está marcado como baja lógica) hay que comenzar a navegar con las sucesivas celdas hasta encontrar la primera baja física (o el error porque el elemento ya existía). Atención que no se puede detenerse en la primera baja lógica y pretender insertarlo allí porque justamente puede estar más adelante. Una vez que se encuentra la primera baja física se lo puede insertar allí o en alguna de las bajas lógicas halladas en ese trayecto.

## Slide 8: Open Addressing or Closed Hashing
Tip Importante:
Para no rebotar de más en las colisiones, lo mejor en el algoritmo de inserción es no insertar en el primer espacio libre que se encuentra, sino en la primera baja lógica que se encontró en el camino hasta descubrir que se podía insertar (se halló baja física).

## Slide 9: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 

## Slide 10: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=1
loadFactor=1/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 

## Slide 11: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 

## Slide 12: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=2
loadFactor=2/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | 
6 | 
7 | 
8 | 
9 | 

## Slide 13: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | 
6 | 
7 | 
8 | 
9 | 

## Slide 14: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=3
loadFactor=3/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 | 

## Slide 15: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 | 

## Slide 16: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=4
loadFactor=4/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | <4, "Sue"> notdeleted
6 | <15, "Meg"> notdeleted
7 | 
8 | 
9 | 

## Slide 17: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> notdeleted
5 | <4, "Sue"> notdeleted
6 | <15, "Meg"> notdeleted
7 | 
8 | 
9 | 

## Slide 18: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=3
loadFactor=3/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> deleted
5 | <4, "Sue"> notdeleted
6 | <15, "Meg"> notdeleted
7 | 
8 | 
9 | 

## Slide 19: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> deleted
5 | <4, "Sue"> notdeleted
6 | <15, "Meg"> notdeleted
7 | 
8 | 
9 | 

## Slide 20: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=2
loadFactor=2/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> deleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 | 

## Slide 21: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> deleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 | 
Fue update
usedKeys=2
loadFactor=2/10

## Slide 22: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <23, "Joe"> deleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 | 

## Slide 23: Open Addressing or Closed Hashing
Caso de Uso C:
initialLookUpSize= 10;
Threshold= 0.75
La fn pre hash el mismo key
myLookUp.insert(3, "Dick");
myLookUp.insert(23, "Joe");
myLookUp.insert(4, "Sue");
myLookUp.insert(15, "Meg");
myLookUp.delete(23); //Joe
myLookUp.delete(15); //Meg
myLookUp.insert(4, "Sue");
myLookUp.insert(43, "Paul");
usedKeys=3
loadFactor=3/10
ranura | Element<K,V>
0 | 
1 | 
2 | 
3 | <3, "Dick"> notdeleted
4 | <43, "Paul"> notdeleted
5 | <4, "Sue"> notdeleted
6 | 
7 | 
8 | 
9 |